## Slide 1
🏠 ApnaGhar v2.0
ESP32 Home Control Using Firebase
Production Release • 13 Engineering Tasks Completed • Firebase + Flutter + Voice AI
Mohammad Sakib Ahmad | @MohammadSakibAhmad0874
October 2026
ESP32
Firebase
Flutter
Alexa

## Slide 2
❌ The Problem
Traditional Home Control is Broken
🔘 Manual Switches Only
No remote control — must be physically present
📡 No Internet Control
Can't turn off AC from office or control from phone
🔋 Power Wasted
No energy monitoring — no idea what consumes how much
🔌 No Safety
No surge protection, no brownout recovery, no watchdog
🔔 No Alerts
Appliance left on? No notification, no awareness
🗣️ No Voice Control
Alexa/Google Home not integrated with local hardware

## Slide 3
✅ Our Solution — Hybrid 3-Mode Architecture
☁️ CLOUD MODE
Via Firebase RTDB
Control from anywhere in the world Real-time WebSocket streaming (<120ms) FCM push notifications
📡 LOCAL MODE
Via mDNS on LAN
Control on local WiFi FastAPI REST endpoint Works when Firebase is slow
📶 OFFLINE MODE
Via ESP32 Access Point
Always-on AP: SmartHome_Control Captive portal on 192.168.4.1 Works with ZERO internet

## Slide 4
🏛️ System Architecture
📱 Flutter App ──────────────────────────────────┐ 💻 Web Dashboard (Vercel) ───────────────────────┤ 🗣️ Alexa Skill (AWS Lambda) ─────────────────────┤──► 🔥 Firebase RTDB ◄══EVENT STREAM══► ⚡ ESP32 🗣️ Google Action (Cloud Functions) ──────────────┤ (apnaghar-3f865) │ 🔘 Physical Wall Switches ───────────────────────┘ │ 📲 FCM Push ──────────────────────────┐ │ ▼ ▼ 📱 Phone Alert ESP32 Hardware Stack: ├── 15s FreeRTOS Watchdog (auto-reboot) ├── ElegantOTA at /update ├── 4× Relay (GPIO 23,22,21,19) ├── PZEM-004T UART Power Meter └── 4× Wall Switch (GPIO 25,26,27,32) └── HLK-PM01 AC-DC + MOV Surge

## Slide 5
⚡ Hardware Design
• ESP32 DevKit V1
Dual-Core 240MHz, 520KB RAM, WiFi+BT
• 4-Relay Module (10A)
JD-VCC isolated, EL817 optocouplers
• PZEM-004T v3.0
UART energy monitor: V/A/W/kWh ±0.5%
• HLK-PM01
AC-DC 5V isolated power supply
• 14D431K MOV
Transient surge clamp <340V
• RC Snubber
100nF X2 + 100Ω 2W — arc suppression
GPIO Pin Mapping
GPIO 23
Relay 1 — Living Room Light
GPIO 22
Relay 2 — Bedroom Lamp
GPIO 21
Relay 3 — Kitchen Light
GPIO 19
Relay 4 — Ceiling Fan
GPIO 25
Switch 1 (50ms debounce)
GPIO 26
Switch 2
GPIO 27
Switch 3
GPIO 32
Switch 4
GPIO 17
PZEM TX
GPIO 16
PZEM RX

## Slide 6
🔥 Firebase — Security & Realtime DB
database.rules.json (Production)
{ "rules": { ".read": false, ".write": false, "devices": { "$deviceId": { ".read": "auth != null && auth.uid == data.child('owner').val()", ".write": "auth != null && auth.uid == data.child('owner').val()", "relays": { ".validate": "newData.hasChildren(['relay1','relay2','relay3','relay4'])" }, "sensors": { ".write": false } } } } }
Firebase RTDB Schema
apnaghar-3f865-rtdb/ └── devices/ └── SH-001/ ├── owner: uid ├── relays/ │ ├── relay1: true/false │ ├── relay2: true/false │ ├── relay3: true/false │ └── relay4: true/false └── sensors/ ├── voltage: 230.5 ├── current: 1.24 ├── power: 285.8 └── energy: 0.048

## Slide 7
✅ All 13 Engineering Tasks — DONE
#1
Firebase SDK Streaming
<120ms WebSocket event-driven (replaces 2s polling)
✅
#2
Firebase Security Rules
Strict UID auth scope — no open read/write
✅
#3
Token Auto-Refresh
TokenHelper.h — OAuth2 refresh before 3600s expiry
✅
#4
PZEM-004T Sensing
V/A/W/kWh ±0.5% via UART (GPIO 16,17)
✅
#5
OTA Updates
ElegantOTA at http://smarthome.local/update
✅
#6
Hardware WDT
15s FreeRTOS Task Watchdog — auto reboot on hang
✅
#7
Custom 2-Layer PCB
8mm HV isolation, KiCad + JLCPCB Gerbers ready
✅
#8
UL94 V-0 Enclosure
Parametric OpenSCAD, dual AC/DC compartment
✅
#9
Voice Assistant Skills
Alexa Smart Home v3 + Google Actions fulfillment
✅
#10
Flutter Release Build
Signed keystore, Play Store AAB generated
✅
#11
FCM Push Notifications
Relay flip + power surge alerts to phone
✅
#12
Manual Wall Switch
GPIO 25-32 debounced, bidirectional cloud sync
✅
#13
Snubber + MOV Circuit
RC 100nF/100Ω + 14D431K clamps <340V
✅

## Slide 8
🛡️ 17 Bugs Found & Fixed
🔴 CRITICAL (4)
• Exposed Firebase API Key in source code
• Open database rules — anyone could read/write
• Brownout reset triggered by relay switching
• 2s HTTP REST polling — high latency + battery drain
🟠 HIGH (5)
• Firebase token expired after 1hr — device disconnected
• No SSL certificate pinning
• Blocking WiFi reconnect hung main loop
• No Hardware Watchdog — device stuck forever on crash
• No OTA update path — needed physical reflash
🟡 MEDIUM + LOW (8)
• No manual switch feedback to cloud
• No inductive load arc suppression (relay damage)
• No energy monitoring
• CORS misconfigured on backend
• + 4 more low-severity UI/UX issues

## Slide 9
🚀 Live Demo
🌐 Web Dashboard
https://web-iota-ruddy-37.vercel.app
📦 GitHub Repository
MohammadSakibAhmad0874
🔥 Firebase Console
apnaghar-3f865
Scan QR codes for live access

## Slide 10
⚡ Firmware Highlights
🔄 Firebase Streaming
📄 firebaseStream.h
Firebase_ESP_Client event listener replaces 2s HTTP polling <120ms relay response time • TokenHelper auto-refreshes OAuth2
⏱️ Hardware Watchdog
📄 watchdog.h
FreeRTOS esp_task_wdt 15s timeout Auto-reboot if main loop hangs (power spike, deadlock)
📡 OTA Updates
📄 otaManager.h
ElegantOTA web UI at http://smarthome.local/update ArduinoOTA for IDE flashing • No physical access needed
💾 NVS Persistence
📄 config.h
WiFi credentials + device ID stored in flash NVS Survives power cuts — auto-reconnects in <5s

## Slide 11
🔌 Custom PCB + 3D Enclosure
Custom 2-Layer PCB
• 100mm × 80mm footprint
• 2oz copper pour, 2-layer
• 8.0mm high-voltage isolation slot (IPC-2221)
• 4× EL817 optocouplers for relay isolation
• HLK-PM01 onboard AC-DC 5V supply
• PZEM-004T header (UART)
• JLCPCB gerber.zip ready for fabrication ($12 for 5 boards)
UL94 V-0 3D Printable Enclosure
• Material: ABS (UL94 V-0 flame retardant)
• Parametric OpenSCAD design
• Dual-compartment: AC side / DC side
• Internal ABS barrier (8mm thick)
• Ventilation slots for airflow
• DIN rail mount points
• Run: openscad enclosure.scad → export STL

## Slide 12
🗣️ Voice Assistant Control
Amazon Alexa — Smart Home v3
"Alexa, turn on the living room light"
"Alexa, turn off bedroom lamp"
"Alexa, turn on all lights"
"Alexa, what is the status of the fan?"
"Alexa, discover my devices"
Google Assistant — Smart Home Actions
"Hey Google, turn on the kitchen light"
"Hey Google, turn off the fan"
"Hey Google, turn on all devices"
"Hey Google, is the bedroom lamp on?"
"Hey Google, sync devices"
Both skills linked to Firebase for realtime device control — no cloud latency

## Slide 13
⚡ Energy Monitoring — PZEM-004T v3.0
Voltage
230.5 V
±0.5%
Current
1.24 A
±0.5%
Active Power
285.8 W
±0.5%
Energy (kWh)
0.048 kWh
±0.5%
Frequency
50.0 Hz
±0.5%
Power Factor
0.98
±0.5%
Connection: PZEM-004T TX→GPIO16, RX→GPIO17 | CT clamp on Live wire only | Isolated 5V supply

## Slide 14
🔗 All Live Links & Artifacts
🌐 Web Dashboard (LIVE)
https://web-iota-ruddy-37.vercel.app
📦 GitHub Repository
https://github.com/MohammadSakibAhmad0874/ESP32-Home-Control-Using-Firebase-System
🔥 Firebase Console
https://console.firebase.google.com/project/apnaghar-3f865
⚡ Vercel Inspector
https://vercel.com/ahmadsakib263-4202s-projects/web
🤖 Railway Backend
https://esp32-home-control-using-firebase-system-production.up.railway.app
📄 APK (local)
./ApnaGhar-v2.0-release.apk
📊 PPTX
./ApnaGhar_v2.0_Presentation.pptx
🔩 Firmware Flash Guide
firmware/HomeControlSketch.ino → Arduino IDE → ESP32 Dev Module

## Slide 15
🚀 Roadmap + Thank You
ApnaGhar is production-ready — here is what comes next:
v2.1
Matter/Thread protocol support (Apple Home, Samsung SmartThings)
v2.2
ESP32-S3 upgrade: USB-OTG, AI accelerator for on-device TinyML
v2.3
Solar panel + battery integration with charging MPPT controller
v2.4
Multi-room grouping + scenes ("Movie Time" = dim + fan + lock)
v3.0
Full local-only mode with Home Assistant integration
🙏 Thank You!
Mohammad Sakib Ahmad | @MohammadSakibAhmad0874 | IoT Engineer
https://github.com/MohammadSakibAhmad0874/ESP32-Home-Control-Using-Firebase-System